Contents

Chapter 1 System Settings	10

Factory Defaults	10

Custom Defaults	11

Scan Mode	12

Level Mode	13

Sense Mode	14

Continuous Mode	15

Read Same Barcode	16

Decoding Timeout	18

Decode Redundancy	19

Aiming LED	20

Illumination Mode	21

Illumination Level	22

Chapter 2 Interface	23

USB HID Keyboard	23

USB Virtual COM Port	24

RS232 COM Port	25

Baud Rate	26

USB Country Keyboard	27

Chapter 3 Symbologies	33

Enable All Symbologies	33

Only Enable 1D Symbologies	34

Only Enable 2D Symbologies	35

EAN-13	36

Transmit Check Character	37

Convert EAN-13 to ISBN	38

Convert EAN-13 to ISSN	39

Enable/Disable Add-On Codes	40

Add-On Code Required	41

EAN-8	42

Transmit Check Character	43

Convert EAN-8 to EAN-13	44

Enable/Disable Add-On Codes	45

Add-On Code Required	46

UPC-A	47

Transmit Preamble Character	48

Transmit Check Character	49

Convert UPC-A to EAN-13	50

Enable/Disable Add-On Codes	51

Add-On Code Required	52

UPC-E	53

Transmit Preamble Character	54

Transmit Check Character	55

Convert UPC-E to UPC-A	56

Enable/Disable Add-On Codes	57

Add-On Code Required	58

Code 128 / GS1 -128	59

Set Lengths for Code 128	60

Code 39	62

Full ASCII	63

Transmit Start/Stop Character	64

Check Character Verification	65

Set Lengths for Code 39	66

Code 32	68

Code 93	69

Set Lengths for Code 93	70

Code 11	72

Transmit Check Character	73

Set Lengths for Code 11	74

Codabar	76

Check Character Verification	77

Transmit Start/Stop Character	78

Set Lengths for Codabar	79

Plessey	81

Set Lengths for Plessey	82

MSI Plessey	84

Check Character Verification	85

Transmit Check Character	86

Set Lengths for MSI Plessey	87

Interleaved 2 of 5	89

Check Character Verification	90

Set Lengths for Interleaved 2 of 5	91

Matrix 2 of 5	93

Set Lengths for Matrix 2 of 5	94

IATA 2 of 5	96

Straight 2 of 5	97

Pharmacode	98

GS1 DataBar 14	99

GS1 DataBar 14 Stacked	100

Transmit Application Identifier “01”	101

GS1 DataBar Expanded	102

GS1 DataBar Expanded Stacked	103

Transmit Application Identifier “01”	104

GS1 DataBar Limited	105

Transmit Application Identifier “01”	106

Composite Code-A	107

Composite Code-B	108

Composite Code-C	109

PDF417	110

Micro PDF417	111

Data Matrix	112

Rectangular Data Matrix	113

QR	114

UTF8/Code Page QR Keyboard Output	115

Micro QR	118

Aztec	119

MaxiCode	120

Chapter 4 String Options	121

Decode Information	122

AIM ID	124

Prefix	125

Suffix	127

Terminated Character	129

Case Conversion	131

Caps Lock	132

GS Code Conversion	133

Function Key Mapping	135

Function Key Output Mode	136

Appendix A - Digit Barcodes	137

Appendix B – Symbologies Table	139

Appendix C - ASCII Code Table	143

Appendix D – Function Key Table	169

Chapter 1 System Settings

Factory Defaults

Enter Setup

Restore All Factory Defaults

Exit Setup

Custom Defaults

Enter Setup

Save as Custom Defaults

Restore All Custom Defaults

Exit Setup

Scan Mode

Level Mode:

A trigger pull activates a decode session. The decode session continues until a barcode is decoded or you release the trigger.

Sense Mode:

The engine activates a decode session every time it detects a barcode presented to it. The decode session continues until a barcode is decoded or the decode session timeout expires.

Continuous Mode:

The engine automatically starts one decode session after another. To suspend/resume barcode reading, simply press the trigger.

Level Mode

Enter Setup

** Level Mode

Exit Setup

Sense Mode

Enter Setup

Sense Mode

Exit Setup

Continuous Mode

Enter Setup

Continuous Mode

Exit Setup

Read Same Barcode

This setting can avoid undesired rereading of same barcode in a given period of time. This feature is only applicable to the Sense and Continuous modes.

Do Not Reread:

Do not allow to reread same barcode when reading same barcode in a given period of time.

Read After Timeout :

Allow the engine to reread same barcode after the reread timeout expires.

It is programmable in 1ms increments from 0ms to 5,000 ms. When it is set to a value greater than 5,000, the timeout for rereading same programming barcode is limited to 5,000 ms. The default setting is Ignore Same Barcode when reading same barcode in 500 ms.

Reread same barcode after 1,00ms:

1. Scan the Enter Setup barcode.

2. Scan the Read After Timeout barcode.

3. Scan the Set Time barcode.

4. Scan the numeric barcodes “1”, “0”, “0” and “0” from the “Digit Barcodes” section

in Appendix.

5. Scan the Exit Setup barcode.

| Read Same Barcode |
| --- |
| Enter Setup |
| **DoNot Reread | Read After Timeout |
| Set Time (ms) |
| Exit Setup |

Decoding Timeout

Decoding Timeout specifies the maximum time the engine will spend decoding an image. This feature is only applicable to the Level and Sense modes.

It is programmable in 1ms increments from 0 ms to 3,600,000 ms. When it is set to a value greater than  3,600,000, the timeout for rereading same programming barcode is limited to 3,600,000 ms. The default timeout is 5000 ms.

Set Decoding Timeout to 1,000 ms:

1. Scan the Enter Setup barcode.

2. Scan the Decoding Timeout barcode.

3. Scan the numeric barcodes “1”, “0”, “0” and “0” from the “Digit Barcodes”

section in Appendix.

4. Scan the Exit Setup barcode.

Enter Setup

Decoding Timeout (ms)

Exit Setup

| Decode Redundancy |
| --- |
| Enter Setup |
| 2 Times | 3 Times |
| **Disable |
| Exit Setup |

| Aiming LED |
| --- |
| Enter Setup |
| Disable | Always On |
| **Normal (Scan On) |
| Exit Setup |

| Illumination Mode |
| --- |
| Enter Setup |
| Disable | Always On |
| **Normal (Scan On) |
| Exit Setup |

| Illumination Level |
| --- |
| Enter Setup |
| Low | Medium |
| **High |
| Exit Setup |

Chapter 2 Interface

USB HID Keyboard

Enter Setup

**USB HID Keyboard

Exit Setup

USB Virtual COM Port

Enter Setup

USB Virtual COM Port

Exit Setup

RS232 COM Port

Enter Setup

RS232 COM Port

Exit Setup

| Baud Rate |
| --- |
| Enter Setup |
| **9600 | 19200 |
| 38400 | 57600 |
| 115200 | 230400 |
| Exit Setup |

| USB Country Keyboard |
| --- |
| Enter Setup |
| ** U.S. (English) | Belgium |
| Britain | Denmark |
| Exit Setup |

| USB Country Keyboard |
| --- |
| Enter Setup |
| France | Germany |
| Italy | Norway |
| Exit Setup |

| USB Country Keyboard |
| --- |
| Enter Setup |
| Portugal | Spain |
| Sweden | Switzerland |
| Exit Setup |

| USB Country Keyboard |
| --- |
| Enter Setup |
| Japan | Hungary |
| Czech Republic | Slovakia |
| Exit Setup |

| USB Country Keyboard |
| --- |
| Enter Setup |
| Romania | Croatia |
| Poland | Turkish Q |
| Exit Setup |

| USB Country Keyboard |
| --- |
| Enter Setup |
| Brazil | Russian |
| Bulgaria |  |
| Exit Setup |

Chapter 3 Symbologies

Enable All Symbologies

Enter Setup

Enable All Symbologies

Exit Setup

Only Enable 1D Symbologies

Enter Setup

Only Enable 1D Symbologies

Exit Setup

Only Enable 2D Symbologies

Enter Setup

Only Enable 2D Symbologies

Exit Setup

EAN-13

Enter Setup

**Enable EAN-13

Disable EAN-13

Exit Setup

Transmit Check Character

Enter Setup

** Transmit EAN-13 Check Character

Do Not Transmit EAN-13 Check Character

Exit Setup

Convert EAN-13 to ISBN

Enter Setup

Convert EAN-13 to ISBN

**Do Not Convert EAN-13 to ISBN

Exit Setup

Convert EAN-13 to ISSN

Enter Setup

Convert EAN-13 to ISSN

**Do Not Convert EAN-13 to ISSN

Exit Setup

Enable/Disable Add-On Codes

Enter Setup

Enable EAN-13 2/5 Add-On Codes

**Disable EAN-132/5 Add-On Codes

Exit Setup

Add-On Code Required When EAN-13 Add-On Code Required is selected, the engine will only read EAN-13 barcodes that contain add-on codes.

Enter Setup

EAN-13 Add-On Code Required

** EAN-13 Add-On Code Not Required

Exit Setup

EAN-8

Enter Setup

**Enable EAN-8

Disable EAN-8

Exit Setup

Transmit Check Character

Enter Setup

** Transmit EAN-8 Check Character

Do Not Transmit EAN-8 Check Character

Exit Setup

Convert EAN-8 to EAN-13

Enter Setup

Convert EAN-8 to EAN-13

**Do Not Convert EAN-8 to EAN-13

Exit Setup

Enable/Disable Add-On Codes

Enter Setup

Enable EAN-8 2/5 Add-On Codes

**Disable EAN-8 2/5 Add-On Codes

Exit Setup

Add-On Code Required When EAN-8 Add-On Code Required is selected, the engine will only read EAN-8 barcodes that contain add-on codes.

Enter Setup

EAN-8 Add-On Code Required

** EAN-8 Add-On Code Not Required

Exit Setup

UPC-A

Enter Setup

**Enable UPC-A

Disable UPC-A

Exit Setup

Transmit Preamble Character

Enter Setup

** Transmit UPC-A Preamble Character

Do Not Transmit UPC-A Preamble Character

Exit Setup

Transmit Check Character

Enter Setup

** Transmit UPC-A Check Character

Do Not Transmit UPC-A Check Character

Exit Setup

Convert UPC-A to EAN-13

Enter Setup

Convert UPC-A to EAN-13

**Do Not Convert UPC-A to EAN-13

Exit Setup

Enable/Disable Add-On Codes

Enter Setup

Enable UPC-A 2/5 Add-On Codes

**Disable UPC-A 2/5 Add-On Codes

Exit Setup

Add-On Code Required When UPC-A Add-On Code Required is selected, the engine will only read UPC-A barcodes that contain add-on codes.

Enter Setup

UPC-A Add-On Code Required

** UPC-A Add-On Code Not Required

Exit Setup

UPC-E

Enter Setup

**Enable UPC-E

Disable UPC-E

Exit Setup

Transmit Preamble Character

Enter Setup

** Transmit UPC-E Preamble Character

Do Not Transmit UPC-E Preamble Character

Exit Setup

Transmit Check Character

Enter Setup

** Transmit UPC-E Check Character

Do Not Transmit UPC-E Check Character

Exit Setup

Convert UPC-E to UPC-A

Enter Setup

Convert UPC-E to UPC-A

**Do Not Convert UPC-E to UPC-A

Exit Setup

Enable/Disable Add-On Codes

Enter Setup

Enable UPC-E 2/5 Add-On Codes

**Disable UPC-E 2/5 Add-On Codes

Exit Setup

Add-On Code Required When UPC-E Add-On Code Required is selected, the engine will only read UPC-E barcodes that contain add-on codes.

Enter Setup

UPC-E Add-On Code Required

** UPC-E Add-On Code Not Required

Exit Setup

Code 128 / GS1 -128

Enter Setup

**Enable Code 128 / GS1-128

Disable Code 128 / GS1-128

Exit Setup

Set Lengths for Code 128

• One Discrete Length

Select this option to decode only Code 128 symbols containing a selected length.

• Two Discrete Lengths

Select this option to decode only Code 128 symbols containing either of two selected lengths.

• Length Within Range

Select this option to decode a Code 128 symbol with a specific length range.

• Any Length

Select this option to decode Code 128 symbols containing any number of characters within the decoder capability.

To decode only Code 128 symbols with 9 characters.

1. Scan the Enter Setup barcode.

2. Scan the One Discrete Length barcode.

3. Scan the numeric barcodes “9” from the “Digit Barcodes” section in Appendix.

4. Scan the Exit Setup barcode.

| Set Lengths for Code 128 |
| --- |
| Enter Setup |
| One Discrete Length | Two Discrete Lengths |
| Length Within Range | ** Any Length |
| Exit Setup |

Code 39

Enter Setup

**Enable Code 39

Disable Code 39

Exit Setup

Full ASCII

Enter Setup

Enable Code 39 Full ASCII

**Disable Code 39 Full ASCII

Exit Setup

Transmit Start/Stop Character

Enter Setup

Transmit Start/Stop Character

**Do Not Transmit Start/Stop Character

Exit Setup

| Check Character Verification |
| --- |
| Enter Setup |
| Transmit Check Character After Verification | Do Not Transmit Check Character After Verification |
| **Disable |
| Exit Setup |

Set Lengths for Code 39

• One Discrete Length

Select this option to decode only Code 39 symbols containing a selected length.

• Two Discrete Lengths

Select this option to decode only Code 39 symbols containing either of two selected lengths.

• Length Within Range

Select this option to decode a Code 39 symbol with a specific length range.

• Any Length

Select this option to decode Code 39 symbols containing any number of characters within the decoder capability.

To decode only those Code 39 symbols containing either 2 or 14 characters.

1. Scan the Enter Setup barcode.

2. Scan the Two Discrete Lengths barcode.

3. Scan the numeric barcodes “0”,“2” from the “Digit Barcodes” section in Appendix.

4. Scan the numeric barcodes “1”,“4” from the “Digit Barcodes” section in Appendix.

5. Scan the Exit Setup barcode.

| Set Lengths for Code 39 |
| --- |
| Enter Setup |
| One Discrete Length | Two Discrete Lengths |
| Length Within Range | ** Any Length |
| Exit Setup |

Code 32

Enter Setup

Enable Code 32

**Disable Code 32

Exit Setup

Code 93

Enter Setup

Enable Code 93

**Disable Code 93

Exit Setup

Set Lengths for Code 93

• One Discrete Length

Select this option to decode only Code 93 symbols containing a selected length.

• Two Discrete Lengths

Select this option to decode only Code 93 symbols containing either of two selected lengths.

• Length Within Range

Select this option to decode a Code 93 symbol with a specific length range.

• Any Length

Select this option to decode Code 93 symbols containing any number of characters within the decoder capability.

To decode Code 93 symbols containing between 4 and 12 characters.

1. Scan the Enter Setup barcode.

2. Scan the Length Within Range barcode.

3. Scan the numeric barcodes “0”,“4” from the “Digit Barcodes” section in Appendix.

4. Scan the numeric barcodes “1”,“2” from the “Digit Barcodes” section in Appendix.

5. Scan the Exit Setup barcode.

| Set Lengths for Code 93 |
| --- |
| Enter Setup |
| One Discrete Length | Two Discrete Lengths |
| Length Within Range | ** Any Length |
| Exit Setup |

Code 11

Enter Setup

Enable Code 11

**Disable Code 11

Exit Setup

Transmit Check Character

Enter Setup

** Transmit Code 11 Check Character

Do Not Transmit Code 11 Check Character

Exit Setup

Set Lengths for Code 11

• One Discrete Length

Select this option to decode only Code 11 symbols containing a selected length.

• Two Discrete Lengths

Select this option to decode only Code 11 symbols containing either of two selected lengths.

• Length Within Range

Select this option to decode a Code 11 symbol with a specific length range.

• Any Length

Select this option to decode Code 11 symbols containing any number of characters within the decoder capability.

To decode only Code 11 symbols with 9 characters.

1. Scan the Enter Setup barcode.

2. Scan the One Discrete Length barcode.

3. Scan the numeric barcodes “9” from the “Digit Barcodes” section in Appendix.

4. Scan the Exit Setup barcode.

| Set Lengths for Code 128 |
| --- |
| Enter Setup |
| One Discrete Length | Two Discrete Lengths |
| Length Within Range | ** Any Length |
| Exit Setup |

Codabar

Enter Setup

**Enable Codabar

Disable Codabar

Exit Setup

| Check Character Verification |
| --- |
| Enter Setup |
| Transmit Check Character After Verification | Do Not Transmit Check Character After Verification |
| **Disable |
| Exit Setup |

Transmit Start/Stop Character

Enter Setup

Transmit Start/Stop Character

**Do Not Transmit Start/Stop Character

Exit Setup

Set Lengths for Codabar

• One Discrete Length

Select this option to decode only Codabar symbols containing a selected length.

• Two Discrete Lengths

Select this option to decode only Codabar symbols containing either of two selected lengths.

• Length Within Range

Select this option to decode a Codabar symbol with a specific length range.

• Any Length

Select this option to decode Codabar symbols containing any number of characters within the decoder capability.

To decode Codabar symbols containing between 4 and 12 characters.

1. Scan the Enter Setup barcode.

2. Scan the Length Within Range barcode.

3. Scan the numeric barcodes “0”,“4” from the “Digit Barcodes” section in Appendix.

4. Scan the numeric barcodes “1”,“2” from the “Digit Barcodes” section in Appendix.

5. Scan the Exit Setup barcode.

| Set Lengths for Codabar |
| --- |
| Enter Setup |
| One Discrete Length | Two Discrete Lengths |
| Length Within Range | ** Any Length |
| Exit Setup |

Plessey

Enter Setup

Enable Plessey

**Disable Plessey

Exit Setup

Set Lengths for Plessey

• One Discrete Length

Select this option to decode only Plessey symbols containing a selected length.

• Two Discrete Lengths

Select this option to decode only Plessey symbols containing either of two selected lengths.

• Length Within Range

Select this option to decode a Plessey symbol with a specific length range.

• Any Length

Select this option to decode Plessey symbols containing any number of characters within the decoder capability.

To decode Plessey symbols containing between 2 and 13 characters.

1. Scan the Enter Setup barcode.

2. Scan the Length Within Range barcode.

3. Scan the numeric barcodes “0”,“2” from the “Digit Barcodes” section in Appendix.

4. Scan the numeric barcodes “1”,“3” from the “Digit Barcodes” section in Appendix.

5. Scan the Exit Setup barcode.

| Set Lengths for Codabar |
| --- |
| Enter Setup |
| One Discrete Length | Two Discrete Lengths |
| Length Within Range | ** Any Length |
| Exit Setup |

MSI Plessey

Enter Setup

**Enable MSI Plessey

Disable MSI Plessey

Exit Setup

| Check Character Verification |
| --- |
| Enter Setup |
| Disable | **One Check Character , MOD10 |
| Two Check Characters , Mod 10/10 | Two Check Characters , Mod 11/10 |
| Exit Setup |

Transmit Check Character

Enter Setup

** Transmit MSI Plessey Check Character

Do Not Transmit MSI Plessey Check Character

Exit Setup

Set Lengths for MSI Plessey

• One Discrete Length

Select this option to decode only MSI Plessey symbols containing a selected length.

• Two Discrete Lengths

Select this option to decode only MSI Plessey symbols containing either of two selected lengths.

• Length Within Range

Select this option to decode a MSI Plessey symbol with a specific length range.

• Any Length

Select this option to decode MSI Plessey symbols containing any number of characters within the decoder capability.

To decode MSI Plessey symbols containing between 3 and 12 characters.

1. Scan the Enter Setup barcode.

2. Scan the Length Within Range barcode.

3. Scan the numeric barcodes “0”,“3” from the “Digit Barcodes” section in Appendix.

4. Scan the numeric barcodes “1”,“2” from the “Digit Barcodes” section in Appendix.

5. Scan the Exit Setup barcode.

| Set Lengths for MSI Plessey |
| --- |
| Enter Setup |
| One Discrete Length | Two Discrete Lengths |
| Length Within Range | ** Any Length |
| Exit Setup |

Interleaved 2 of 5

Enter Setup

**Enable Interleaved 2 of 5

Disable Interleaved 2 of 5

Exit Setup

| Check Character Verification |
| --- |
| Enter Setup |
| Transmit Check Character After Verification | Do Not Transmit Check Character After Verification |
| **Disable |
| Exit Setup |

Set Lengths for Interleaved 2 of 5

• One Discrete Length

Select this option to decode only Interleaved 2 of 5 symbols containing a selected length.

• Two Discrete Lengths

Select this option to decode only Interleaved 2 of 5 symbols containing either of two selected lengths.

• Length Within Range

Select this option to decode a Interleaved 2 of 5 symbol with a specific length range.

• Any Length

Select this option to decode Interleaved 2 of 5 symbols containing any number of characters within the decoder capability.

To decode only Interleaved 2 of 5 symbols with 8 characters.

1. Scan the Enter Setup barcode.

2. Scan the One Discrete Length barcode.

3. Scan the numeric barcodes “8” from the “Digit Barcodes” section in Appendix.

4. Scan the Exit Setup barcode.

| Set Lengths for Interleaved 2 of 5 |
| --- |
| Enter Setup |
| One Discrete Length | Two Discrete Lengths |
| Length Within Range | ** Any Length |
| Exit Setup |

Matrix 2 of 5

Enter Setup

Enable Matrix 2 of 5

**Disable Matrix 2 of 5

Exit Setup

Set Lengths for Matrix 2 of 5

• One Discrete Length

Select this option to decode only Matrix 2 of 5 symbols containing a selected length.

• Two Discrete Lengths

Select this option to decode only Matrix 2 of 5 symbols containing either of two selected lengths.

• Length Within Range

Select this option to decode a Matrix 2 of 5 symbol with a specific length range.

• Any Length

Select this option to decode Matrix 2 of 5 symbols containing any number of characters within the decoder capability.

To decode only Matrix 2 of 5 symbols with 8 characters.

1. Scan the Enter Setup barcode.

2. Scan the One Discrete Length barcode.

3. Scan the numeric barcodes “8” from the “Digit Barcodes” section in Appendix.

4. Scan the Exit Setup barcode.

| Set Lengths for Interleaved 2 of 5 |
| --- |
| Enter Setup |
| One Discrete Length | Two Discrete Lengths |
| Length Within Range | ** Any Length |
| Exit Setup |

IATA 2 of 5

Enter Setup

Enable IATA 2 of 5

**Disable IATA 2 of 5

Exit Setup

Straight 2 of 5

Enter Setup

Enable Straight 2 of 5

**Disable Straight 2 of 5

Exit Setup

Pharmacode

Enter Setup

Enable Pharmacode

**Disable Pharmacode

Exit Setup

GS1 DataBar 14

Enter Setup

**Enable GS1 DataBar 14

Disable GS1 DataBar 14

Exit Setup

GS1 DataBar 14 Stacked

Enter Setup

Enable GS1 DataBar 14 Stacked

**Disable GS1 DataBar 14 Stacked

Exit Setup

Transmit Application Identifier “01”

Enter Setup

** Transmit Application Identifier “01”

Do Not Transmit Application Identifier “01”

Exit Setup

GS1 DataBar Expanded

Enter Setup

**Enable GS1 DataBar Expanded

Disable GS1 DataBar Expanded

Exit Setup

GS1 DataBar Expanded Stacked

Enter Setup

Enable GS1 DataBar Expanded Stacked

**Disable GS1 DataBar Expanded Stacked

Exit Setup

Transmit Application Identifier “01”

Enter Setup

** Transmit Application Identifier “01”

Do Not Transmit Application Identifier “01”

Exit Setup

GS1 DataBar Limited

Enter Setup

**Enable GS1 DataBar Limited

Disable GS1 DataBar Limited

Exit Setup

Transmit Application Identifier “01”

Enter Setup

** Transmit Application Identifier “01”

Do Not Transmit Application Identifier “01”

Exit Setup

Composite Code-A

Enter Setup

Enable Composite Code-A

**Disable Composite Code-A

Exit Setup

Composite Code-B

Enter Setup

Enable Composite Code-B

**Disable Composite Code-B

Exit Setup

Composite Code-C

Enter Setup

Enable Composite Code-C

**Disable Composite Code-C

Exit Setup

PDF417

Enter Setup

**Enable PDF417

Disable PDF417

Exit Setup

Micro PDF417

Enter Setup

**Enable Micro PDF417

Disable Micro PDF417

Exit Setup

Data Matrix

Enter Setup

**Enable Data Matrix

Disable Data Matrix

Exit Setup

Rectangular Data Matrix

Enter Setup

**Enable Rectangular Data Matrix

Disable Rectangular Data Matrix

Exit Setup

QR

Enter Setup

**Enable QR

Disable QR

Exit Setup

UTF8/Code Page QR Keyboard Output

Enter Setup

** GB2312 – Unicode / Excel ; Notepad

GB2312 – Code Page / Word

Exit Setup

| UTF8/Code Page QR Keyboard Output |
| --- |
| Enter Setup |
| Thailand | Russia |
| Turkey | Brazil |
| Exit Setup |

| UTF8/Code Page QR Keyboard Output |
| --- |
| Enter Setup |
| Germany | Italy |
| Spain | Portugal |
| Exit Setup |

Micro QR

Enter Setup

**Enable Micro QR

Disable Micro QR

Exit Setup

Aztec

Enter Setup

Enable Aztec

**Disable Aztec

Exit Setup

MaxiCode

Enter Setup

Enable MaxiCode

**Disable MaxiCode

Exit Setup

Chapter 4 String Options

This chapter describes the alterations which can be made to the format of transmitted data string.

Options available are:

- Case Conversion

- Transmission of Decode Information

- Transmission of AIM ID

- Transmission of Prefix / Suffix

- Transmission of Terminated Character (postamble)

- Function Key Mapping

- GS Code Conversion

The string format transmitted as following figure:

| Barcode Contents (4 bytes) | Prefix (8 bytes) | AIM identify ID | Barcode Data | Suffix (8 bytes) | Terminated Character (1 byte) |
| --- | --- | --- | --- | --- | --- |

Decode Information

Decode information specifies the identify code and length of decoded barcode. This feature is only applicable to RS232 interface.

The barcode information transmitted as following figure:

| Star Code 0x03 (1 byte) | Identify Code (1 byte) | Code Length (2 bytes) 0x0001 ~0xFFFF |
| --- | --- | --- |

Value of Identify Code：

| ID | 2D Symbologies | ID | 1D Symbologies | ID | 1D Symbologies |
| --- | --- | --- | --- | --- | --- |
| 0x41 | PDF417 | 0x61 | UPC A | 0x71 | Pharmacode |
| 0x42 | Micro PDF417 | 0x62 | UPC E | 0x72 | GS1 DataBar 14 |
| 0x43 | Data Matrix | 0x63 | EAN 8 | 0x73 | GS1 DataBar Expanded |
| 0x44 | QR | 0x64 | EAN 13 | 0x74 | GS1 DataBar Limited |
| 0x45 | Micro QR | 0x65 | Code 128 | 0x75 | Composite Code-A |
| 0x46 | Aztec | 0x66 | Code 39 | 0x76 | Composite Code-B |
| 0x47 | MaxiCode | 0x67 | Code 93 | 0x77 | Composite Code-C |
|  |  | 0x68 | Code 32 |  |  |
|  |  | 0x69 | Code 11 |  |  |
|  |  | 0x6A | Codabar |  |  |
|  |  | 0x6B | Plessey |  |  |
|  |  | 0x6C | MSI Plessey |  |  |
|  |  | 0x6D | Interleaved 2 of 5 |  |  |
|  |  | 0x6E | IATA 2 of 5 |  |  |
|  |  | 0x6F | Matrix 2 of 5 |  |  |
|  |  | 0x70 | Straight 2 of 5 |  |  |
| Decode Information Enter Setup Enable **Disable Exit Setup AIM ID Enter Setup Enable AIM ID **Disable AIM ID Exit Setup |

Prefix

Maximum 8 characters can include in front of data string.

Set ASCII code “a” for all Symbologies

1. Scan the Enter Setup barcode.

2. Scan the Set All Symbologies barcode.

3. Scan the “a” barcode from the ASCII Code Table in Appendix C.

4. Scan the Exit Setup barcode.

Disable Prefix for all Symbologies

1. Scan the Enter Setup barcode.

2. Scan the Disable All Symbologies barcode.

3. Scan the Exit Setup barcode.

Set “E”,”1” for EAN 13

1. Scan the Enter Setup barcode.

2. Scan the Set Symbology barcode.

3. Scan the EAN 13 barcode in Appendix - B.

4. Scan the “E” barcode from the ASCII Code Table in Appendix C.

5. Scan the “1” barcode from the ASCII Code Table in Appendix C.

6. Scan the Exit Setup barcode.

Disable Prefix for EAN 13

1. Scan the Enter Setup barcode.

2. Scan the Disable Symbology barcode.

3. Scan the EAN 13 barcode from the Symbologies Table in Appendix - B.

4. Scan the Exit Setup barcode.

| Enter Setup |
| --- |
| **Disable All Symbologies | Set All Symbologies |
| Set Symbology | Disable Symbology |
| Exit Setup |

Suffix

Maximum 8 characters can include in end of data string.

Set ASCII code “a” for all Symbologies

1. Scan the Enter Setup barcode.

2. Scan the Set All Symbologies barcode.

3. Scan the “a” barcode from the ASCII Code Table in Appendix C.

4. Scan the Exit Setup barcode.

Disable Prefix for all Symbologies

1. Scan the Enter Setup barcode.

2. Scan the Disable All Symbologies barcode.

3. Scan the Exit Setup barcode.

Set “S”,”2” for EAN-8

1. Scan the Enter Setup barcode.

2. Scan the Set Symbology barcode.

3. Scan the EAN 8 barcode in Appendix - B.

4. Scan the “S” barcode from the ASCII Code Table in Appendix C.

5. Scan the “2” barcode from the ASCII Code Table in Appendix C.

6. Scan the Exit Setup barcode.

Disable Prefix for EAN 8

1. Scan the Enter Setup barcode.

2. Scan the Disable Symbology barcode.

3. Scan the EAN 8 barcode from the Symbologies Table in Appendix - B.

4. Scan the Exit Setup barcode.

| Enter Setup |
| --- |
| **Disable All Symbologies | Set All Symbologies |
| Set Symbology | Disable Symbology |
| Exit Setup |
| Terminated Character |
| Enter Setup |
| Disable |
| **CR |
| Exit Setup |

Terminated Character

Enter Setup

CR / LF

TAB

Exit Setup

| Case Conversion |
| --- |
| Enter Setup |
| Convert All to Upper Case | Convert All to Lower Case |
| **Disable |
| Exit Setup |
| Caps Lock |
| Enter Setup |
| **Disable Caps Lock |
| Enable Caps Lock |
| Exit Setup |

GS Code Conversion

Convert GS code to other ASCII Code

设置 GS字元转换为 # 输出:

1. 扫描 "Enter Setup"

2. 扫描 "转换GS字元"

3. 扫描 ASCII Code 表， # 设置码

4. 扫描 "Exit Setup"

设置 GS字元转换为回车输出:

1. 扫描 "Enter Setup"

2. 扫描 "转换GS字元"

3. 扫描 ASCII Code 表，回车 设置码

4. 扫描 "Exit Setup"

恢复GS字元默认值

1. 扫描 "Enter Setup"

2. 扫描 "关闭GS字元转换"

3. 扫描 "Exit Setup"

GS Code Conversion

Enter Setup

**Disable GS Conversion

Enable GSConversion

Exit Setup

Function Key Mapping

Enter Setup

Disable

**Enable

Exit Setup

Function Key Output Mode

Enter Setup

**Ctrl Char Mode

Alt + Unicode Mode

Exit Setup

Appendix A - Digit Barcodes

| 0 | 1 |
| --- | --- |
| 2 | 3 |
| 4 | 5 |

Appendix A - Digit Barcodes

| 6 | 7 |
| --- | --- |
| 8 | 9 |

Appendix B – Symbologies Table

| UPC A | UPC E |
| --- | --- |
| EAN 8 | EAN 13 |
| Code 128 | Code 39 |
| Code 93 | Code 32 |

Appendix B – Symbologies Table

| Code 11 | Codabar |
| --- | --- |
| Plessey | MSI Plessey |
| Interleaved 2 of 5 | IATA 2 of 5 |
| Matrix 2 of 5 | Straight 2 of 5 |

Appendix B – Symbologies Table

| Pharmacode | GS1 DataBar 14 |
| --- | --- |
| GS1 DataBar Expanded | GS1 DataBar Limited |
| GS1 DataBar 14 Stacked | GS1 DataBar Expanded Stacked |
| Composite Code-A | Composite Code-B |

Appendix B – Symbologies Table

| Composite Code-C | PDF417 |
| --- | --- |
| Micro PDF417 | Data Matrix |
| QR | Micro QR |
| Aztec | MaxiCode |

Appendix C - ASCII Code Table

| Hexadecimal | Decimal | ASCII | Function Key Mapping |
| --- | --- | --- | --- |
|  |  |  | Ctrl Char模式 | Alt+Unicode模式 |
| 00 | 0 | Null | Ctrl+@ | Alt + 000 |
| 01 | 1 | Home | Ctrl+A | Alt + 001 |
| 02 | 2 | End | Ctrl+B | Alt + 002 |
| 03 | 3 | Up Arrow | Ctrl+C | Alt + 003 |
| 04 | 4 | Down Arrow | Ctrl+D | Alt + 004 |
| 05 | 5 | Left Arrow | Ctrl+E | Alt + 005 |
| 06 | 6 | Right Arrow | Ctrl+F | Alt + 006 |
| 07 | 7 | Null | Ctrl+G | Alt + 007 |
| 08 | 8 |  | Backspace | Backspace | Alt + 008 |
| 09 | 9 |  | TAB | TAB | Alt + 009 |
| 0A | 10 | Null | Ctrl+J | Alt + 010 |
| 0B | 11 | Null | Ctrl+K | Alt + 011 |
| 0C | 12 | Null | Ctrl+L | Alt + 012 |
| 0D | 13 |  | Enter | Enter | Enter |
| 0E | 14 | Page Up | Ctrl+N | Alt + 014 |
| 0F | 15 | Page Down | Ctrl+O | Alt + 015 |

| Hexadecimal | Decimal | ASCII | Function Key Mapping |
| --- | --- | --- | --- |
|  |  |  | Ctrl Char模式 | Alt+Unicode模式 |
| 10 | 16 | F11 | Ctrl+P | Alt + 016 |
| 11 | 17 | figu Null | Ctrl+Q | Alt + 017 |
| 12 | 18 | Null | Ctrl+R | Alt + 018 |
| 13 | 19 | Null | Ctrl+S | Alt + 019 |
| 14 | 20 | Null | Ctrl+T | Alt + 020 |
| 15 | 21 | F12 | Ctrl+U | Alt + 021 |
| 16 | 22 | F1 | Ctrl+V | Alt + 022 |
| 17 | 23 | F2 | Ctrl+W | Alt + 023 |
| 18 | 24 | F3 | Ctrl+X | Alt + 024 |
| 19 | 25 | F4 | Ctrl+Y | Alt + 025 |
| 1A | 26 | F5 | Ctrl+Z | Alt + 026 |
| 1B | 27 | F6 | Ctrl+[ | Alt + 027 |
| 1C | 28 | F7 | Ctrl+\ | Alt + 028 |
| 1D | 29 | F8 | Ctrl+] | Alt + 029 |
| 1E | 30 | F9 | Ctrl+^ | Alt + 030 |
| 1F | 31 | F10 | Ctrl+_ | Alt + 031 |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 20 | 32 | SPACE |  |
| 21 | 33 | ! |  |
| 22 | 34 | " |  |
| 23 | 35 | # |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 24 | 36 | $ |  |
| 25 | 37 | % |  |
| 26 | 38 | & |  |
| 27 | 39 | ' |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 28 | 40 | ( |  |
| 29 | 41 | ) |  |
| 2A | 42 | * |  |
| 2B | 43 | + |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 2C | 44 | , |  |
| 2D | 45 | - |  |
| 2E | 46 | . |  |
| 2F | 47 | / |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 30 | 48 | 0 |  |
| 31 | 49 | 1 |  |
| 32 | 50 | 2 |  |
| 33 | 51 | 3 |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 34 | 52 | 4 |  |
| 35 | 53 | 5 |  |
| 36 | 54 | 6 |  |
| 37 | 55 | 7 |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 38 | 56 | 8 |  |
| 39 | 57 | 9 |  |
| 3A | 58 | : |  |
| 3B | 59 | ; |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 3C | 60 | < |  |
| 3D | 61 | = |  |
| 3E | 62 | > |  |
| 3F | 63 | ? |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 40 | 64 | @ |  |
| 41 | 65 | A |  |
| 42 | 66 | B |  |
| 43 | 67 | C |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 44 | 68 | D |  |
| 45 | 69 | E |  |
| 46 | 70 | F |  |
| 47 | 71 | G |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 48 | 72 | H |  |
| 49 | 73 | I |  |
| 4A | 74 | J |  |
| 4B | 75 | K |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 4C | 76 | L |  |
| 4D | 77 | M |  |
| 4E | 78 | N |  |
| 4F | 79 | O |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 50 | 80 | P |  |
| 51 | 81 | Q |  |
| 52 | 82 | R |  |
| 53 | 83 | S |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 54 | 84 | T |  |
| 55 | 85 | U |  |
| 56 | 86 | V |  |
| 57 | 87 | W |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 58 | 88 | X |  |
| 59 | 89 | Y |  |
| 5A | 90 | Z |  |
| 5B | 91 | [ |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 5C | 92 | \ |  |
| 5D | 93 | ] |  |
| 5E | 94 | ^ |  |
| 5F | 95 | _ |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 60 | 96 | ` |  |
| 62 | 97 | a |  |
| 62 | 98 | b |  |
| 63 | 99 | c |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 64 | 100 | d |  |
| 65 | 101 | e |  |
| 66 | 102 | f |  |
| 67 | 103 | g |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 68 | 104 | h |  |
| 69 | 105 | i |  |
| 6A | 106 | j |  |
| 6B | 107 | k |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 6C | 108 | l |  |
| 6D | 109 | m |  |
| 6E | 110 | n |  |
| 6F | 111 | o |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 70 | 112 | p |  |
| 71 | 113 | q |  |
| 72 | 114 | r |  |
| 73 | 115 | s |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 74 | 116 | t |  |
| 75 | 117 | u |  |
| 76 | 118 | v |  |
| 77 | 119 | w |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 78 | 120 | x |  |
| 79 | 121 | y |  |
| 7A | 122 | z |  |
| 7B | 123 | { |  |

| Hexadecimal | Decimal | ASCII |
| --- | --- | --- |
| 7C | 124 | ¦ |  |
| 7D | 125 | } |  |
| 7E | 126 | ~ |  |
| 7F | 127 | Delete |  |

Appendix D – Function Key Table

| Insert | Delete |
| --- | --- |
| Home | End |
| Up Arrow | Down Arrow |
| Left Arrow | Right Arrow |

Appendix D – Function Key Table

| Shift | ESC |
| --- | --- |
| Page Up | Page Down |
| F1 | F2 |
| F3 | F4 |

Appendix D – Function Key Table

| F5 | F6 |
| --- | --- |
| F7 | F8 |
| F9 | F10 |
| F11 | F12 |